## Slide 1: New Automation Technology Beckhoff Automation

## Slide 2: XTS Training

## Slide 3: XTS | a new dimension for intelligent product transport
linear
rotary
Notes: XTS combines advantages of rotary and linear systems

## Slide 4: Agenda | XTS- Overview
System properties
XTS-StarterKit
XTS Module
Preparation and Assembly
First Test
Rail mounting
Rerailing of Mover

## Slide 5: System properties
mover identification (standard and Mover 1)
20 kg payload, even more in coupled
operation
20
speed up to 4 m/s – acceleration up to 10 m/s²
repeat accuracy
down to (±) 10 µm
center-to-center distance
of 50 mm possible
1

## Slide 6: XTS technical data
Alignment | horizontally, vertically or at any angle from 1…179° | 
Magnet pitch | ≥ 50 mm | 
Peak force | AT9001-x550 (5-pin): 100 N, AT9001-xAA0 (10-pin): 210 N | AT9001-x775 (7-pin): 130 N, (specifications refer to straight sections)
Continuous force | AT9001-x550 (5-pin): 30 N, AT9001-xAA0 (10-pin): 75 N | AT9001-x775 (7-pin): 45 N, (specifications refer to straight sections)
Max. speed | 4 m/s | 
Max. payload | up to 40 kg | higher loads with reduced dynamics possible
Max. acceleration | 10 g | without payload
Absolute accuracy | ±0.25 mm | within a straight module
Repeatability | < ±0.01 mm | standstill unidirectional
Synchronization accuracy | < ±0.15 mm | at 1.5 m/s within straight motor module
Max. system size | > 100 m, > 200 mover | 
IP protection rating | IP65 | in assembled condition for a closed system
Approvals/markings | CE, UL | 

## Slide 7: Agenda | XTS- Assembly
XTS-StarterKit
XTS Module
Preparation and Assembly
First Test
Rail mounting
Rerailing of Mover

## Slide 8: XTS StarterKit

## Slide 9: XTS starter kits
XTS starter kits
plug-and-play solutions for office environments
XTS starter kits
first mover movements possible with little effort
XTS starter kits
one day of support and programming assistance

## Slide 10: XTS starter kits
AT2000-0500
starter kit small, 500 mm straight length
AT2000-1000
starter kit medium, 1000 mm straight length
AT2000-1500
starter kit large, 1500 mm straight length

## Slide 11: Agenda | XTS- Assembly
XTS-StarterKit
XTS Module
Preparation and Assembly
First Test
Rail mounting
Rerailing of Mover

## Slide 12: XTS Modules
Straight and curved motor module
Industrial PC with TwinCAT NC PTP, TwinCAT XTS Extension
Mover
Guide rail

## Slide 13: XTS Modules The XTS motor module
Straight and curved motor module
Industrial PC with TwinCAT NC PTP, TwinCAT XTS Extension
Mover
Guide rail

## Slide 14: XTS Modules The XTS motor module
Fully integrated interface for machine bed and guide rail
Fully integrated motor function and multi-position detection
Fully integrated power supply and data communication

## Slide 15: XTS Modules The XTS motor module
motor, coil package
EtherCAT and power supply
(control: 24 V DC, power: 48 V DC)
mechanical interface for the guide rail
power electronics and displacement measurement
mechanical interface for the support structure

## Slide 16: XTS Modules The XTS motor module
power supply, EtherCAT
  motor modules with/without supply cables
  supply can be connected internally across motor modules
  supply voltage in the protective low voltage range
power electronics
  output stages integrated in coil package
  temperature monitoring of output stage
  temperature model of the coils for optimum peak load utilization (I²T model)

## Slide 17: XTS Modules The XTS motor module
position feedback
  non-contact position detection with an encoder flag attached to the mover
  absolute accuracy of ± 0.25 mm
  positions are available immediately after switching on
     no homing necessary
  multi-position detection: no position restrictions even at the module limits

## Slide 18: XTS Modules The XTS motor module

## Slide 19: XTS Modules The XTS motor module / Other geometries
180° curve (clothoid) in 500 mm
-22.5° curve in 250 mm for Ø 1273 mm
45° curve in 250 mm for Ø 637 mm
22.5° curve in 250 mm for Ø 1273 mm

## Slide 20: XTS Modules The XTS motor module /Flexible track layouts

## Slide 21: XTS Modules System solution – mover and guide rail
Straight and curved motor module
Industrial PC with TwinCAT NC PTP, TwinCAT XTS Extension
Mover
Guide rail

## Slide 22: XTS Modules System solution – mover and guide rail
Beckhoff system solution
Guide rail system, mounted parallel with the motor modules

## Slide 23: XTS Modules System solution – mover and guide rail
Plastic rollers on aluminum guide rail
no need for constant lubrication
Guide rail mounted on motor module
low total costs
Modular system offers expansion options
flexibly adaptation

## Slide 24: XTS Modules Beckhoff: plastic rollers on aluminium rail
Standard mover
Mover for increased payload
Mover for longer service life
Various product versions for different application requirements

## Slide 25: XTS Modules System solution – mover and guide rail
300 g standard payload, even more mass in tests
300
center-to-center distance min. 60 mm
30,000 km mileage with Ø 1.5 m/s during long-term test
600 g standard payload, even more mass in tests
600
center-to-center distance min. 70 mm
25,000 km service life with Ø 1.5 m/s during long-term test

## Slide 26: XTS Modules Beckhoff: plastic rollers on aluminum rail
guide rail made of aluminium
  straight and curved segments
  abrasion-resistant hard anodised aluminium surface
  simple assembly of the guide rail via mechanical interface on the motor module
mover with plastic rollers
  backlash-free running through optimized geometry
  no lubrication necessary
  spring-loaded rollers reduce service interval
magnetic plates
rollers
encoder flag for position feedback
spring-loaded rollers

## Slide 27: Application example: Cosmetics filling line – Groninger & Co. GmbH, Germany

## Slide 28: XTS Modules Guide rail system mounted parallel with the motor modules
Parallel guide rail absorbs weight forces
high payloads
Steel rollers on steel guide rail
high durability
Movers with different magnet plate sets
high process forces supported

## Slide 29: XTS Modules Guide rail system mounted parallel with the motor modules
guidance system routed in parallel to accept higher process forces
hardened steel V-guide to ensure high accuracy over prolonged periods of time
with automatic lubrication system  lubricant is fed to the guide surfaces of the rails
1-track: rail system for 180° curve (clothoid)
PRT2: rail system for round, oval and rectangular systems
motor modules available with upper profile without drill holes
   increased ease of cleaning

## Slide 30: Application example: Optical inspection system – GEFASOFT, Germany
Notes: GEFASOFT Automatisierung und Software GmbH, Deutschland

## Slide 31: XTS Modules guide rail and movers Comparison
Beckhoff system solution
Guide rail system, mounted parallel with the motor modules
higher loads
higher process forces
maximised service life
highest level of dynamics
low costs
lubricant-free

## Slide 32: XTS Modules The control system
Straight and curved motor module
Industrial PC with TwinCAT NC PTP, TwinCAT XTS Extension
Mover
Guide rail

## Slide 33: XTS Modules The control system
PC-based control
Data is available centrally (diagnostics, predictive maintenance ...)
PC-based control
real-time coupling between process and hardware
PC-based control
suitable configurations for controlling the overall process

## Slide 34: XTS Modules The control system | TwinCAT3

## Slide 35: XTS Modules The control system | functions for XTS programming
easy handling of desired movements
All motion control functions are available: flying saw, electrical gear unit, cam plates …
XTS Extension
Motion Control
functional extensions handle typical XTS requirements
automatic accumulation, collision and jerk avoidance, centrifugal force limitation
HMI
creating visualizations with a single mouse click
extensive visualization options with TwinCAT3
Different levels of detail enable easy system diagnostics.

## Slide 36: XTS Modules The control system | XTS Extension
XTS software
Integrated simulation functions facilitate plant design
XTS software
Software tools simplify configuration
XTS software
Motion control function blocks reduce engineering effort

## Slide 37: XTS Modules The control system | functions for XTS programming
From the point of view of application programming, a mover appears like a “normal” servo axis
XTS Extension
XTS extension
NC functions
Application software
XTS Modules

## Slide 38: XTS Modules The control system | functions for XTS programming
The XTS extension in TwinCAT decouples servo algorithms from the hardware components and calculates them centrally.
XTS Extension
PC platform
Mover 1
Mover 2
Mover m
Virtual connection
PLC
1st axis
TwinCAT Motion Control, PTP
2nd axis
mth axis

## Slide 39: XTS Modules The control system | functions for XTS programming
PC platform
Mover 1
Mover 2
Mover m
PLC
1st axis
TwinCAT Motion Control, PTP
2nd axis
mth axis
Motion Control
all motion control functions are available, e.g.
  flying saw
  electrical gear unit
  cam plates

## Slide 40: XTS Modules The control system | functions for XTS programming
PC platform
Mover 1
Mover 2
Mover m
PLC
1st axis
TwinCAT Motion Control, PTP
2nd axis
mth axis
Motion Control
functional extensions handle typical XTS requirements
  automatic accumulation
  collision and jerk avoidance
  centrifugal force limitation

## Slide 41: XTS Modules The control system | XTS Extension
PC platform
The XTS extension in TwinCAT decouples servo algorithms from the hardware components and calculates them centrally.
Mover 1
Mover 2
Mover m
Virtual connection
PLC
1st axis
TwinCAT Motion Control, PTP
2nd axis
mth axis

## Slide 42: XTS Modules The control system | XTS Extension
From the point of view of application programming, a mover appears like a “normal” servo axis
all motion control functions are available, e.g.
  flying saw
  electrical gear unit
  cam plates
functional extensions handle typical XTS requirements
  automatic accumulation
  collision and jerk avoidance
  centrifugal force limitation
XTS extension
NC functions
Application software
XTS Modules

## Slide 43: XTS Modules The control system | HMI Control
HMI
XTS HMI Control offers visualization options for the machine operator

## Slide 44: XTS Modules The control system | HMI Control
HMI
EC-Diag HMI Control offers visualization options for the machine operator

## Slide 45: XTS | New Freedom in Machine Building
Complex sequences – simplified solution: XTS

## Slide 46: Training material
This training material is provided to complement the presented training content. Outside the actual training the material may only be used for internal purposes at the company of the course participant. In addition, the material or extracts thereof may be used in end customer training for products containing Beckhoff products, or for presentations, provided the presentation refers to Beckhoff products. Extracts or copies of the training material must contain the following copyright acknowledgement: “© Beckhoff Automation GmbH & Co. KG”.
The same applies to extracts from presentation material. The user of the material is solely responsible for the completeness of extracts and copies. It is explicitly not permitted to offer commercial or free training for Beckhoff products. This applies to training with and or without the training material. The training material must not be edited, manipulated or modified.
Passing on of the aforementioned rights to third parties is not permitted.
Beckhoff Automation GmbH & Co. KG

## Slide 47
02/2021