## Slide 1: New Automation Technology Beckhoff Automation

## Slide 2: XTS Training

## Slide 3: Agenda | XTS- Assembly
XTS-StarterKit
Preparation and Assembly
First Test
Rail mounting
Rerailing of Mover

## Slide 4: XTS StarterKit

## Slide 5: XTS StarterKit
AT2000-0500 starter kit small, 500 mm straight length
AT2000-1000 starter kit medium, 1000 mm straight length
AT2000-1500 starter kit large, 1500 mm straight length

## Slide 6: Agenda | XTS- Assembly
XTS-StarterKit
Preparation and Assembly
First Test
Rail mounting
Rerailing of Mover

## Slide 7: Prepare the XTS Modules
Insert all pins on the bottom side of the frame
Insert the pins to the rail
Insert the pins to the neighbor modules
  4x D5x10 A2 DIN 7
  1x D5x30 A2 DIN 7

## Slide 8: Prepare the XTS Modules
Insert O-ring (as sealing) on
the side of the module
Insert the connection PCB
Notes: AWB – Text in pictures:
Left photo:
“The printed nameplate of the motor module and PCB face the same direction for proper assembly”
Right photo:
“Carefully insert the PCB into the internal connector of the motor module. Note the position of the connector with smaller pin package at the bottom.”

## Slide 9: Prepare the XTS Modules

## Slide 10: Module frame mounting
Beginning with the straight infeed module
Following with all other straights from both sides of the frame
The electrical connection is done by sliding the connection PCB in the neighbouring module

## Slide 11: Module frame mounting
Fix the modules with
  Screw M5x20 Cyl. A2 DIN 912
  Washer M5 A2 DIN 9021
Do not tighten the screws to allow for adjustment of the modules
!

## Slide 12: Prepare the XTS Modules
Mount the curve modules last
The curves will meet the straights as you tighten the screws to the frame
  1 x Pin D5x30 A2 DIN 7
  3 (2)x Pin D5x10 A2 DIN 7
  (1) x Pin D5x8 A2 DIN 7  lower HW28
  1 x O-ring (as sealing)
  1 x Connection PCB
  Screw M5x30 Cyl. A2 DIN 912 &
  Washer M5 A2 DIN 9021

## Slide 13: Module frame mounting
insert 1mm aluminum sheet at one side
  Only before HW..
    HW03 at 0.5m HW02 at 1.0m
    HW02 at 1.5m

## Slide 14: Module frame mounting
Pin out of the infeed module as labelled on the name plate and cable
Connect EtherCAT to the IPC or CU2508
PIN | Signal
1 | 48V
2 | GND 48V
3 | 24V
4 | GND 24V

## Slide 15: Agenda | XTS- Assembly
XTS-StarterKit
Preparation and Assembly
First Test
Rail mounting
Rerailing of Mover

## Slide 16: HardWare Scan | Opening a TC3 solution
TwinCAT 3 Engineering (XAE) is started via the TwinCAT icon.
TwinCAT 3 icon
1
2

## Slide 17: HardWare Scan | Creating a new project
Create a new project via the start page or the New Project icon.
Select a project name and storage location and confirm with OK.

## Slide 18: HardWare Scan | change to target system
When a new project is created,
the local target system “<Local>” is automatically selected.
Change to your XTS target system
The target system selection box shows the active target system.

## Slide 19: HardWare Scan | Scan HW-devices
The devices connected to the target system can be scanned. i.e. the fieldbus connections or the devicespecific modules such as the Novram in the IPC
In the Solution Explorer, right-click on “Devices” under I/O and select Scan
A device scan is only possible from a target system that is in Config mode.

## Slide 20: HardWare Scan | found HW-devices
Once the scan has been completed all the hardware should have been found
The first module is the straight section infeed module.
  AT2001-0250
Each module includes
  a motor module (AT200X-0250 or AT2050-0500)
  and a sensor lines (AT200X-5250 or AT2050-5501

## Slide 21: Agenda | XTS- Assembly
XTS-StarterKit
Preparation and Assembly
First Test
Rail mounting
Rerailing of Mover

## Slide 22: Rail module mounting
Screw the rail onto the system, beginning with the straight and finish with the two curves
  Screw M4x40 Cyl. A2 DIN 912
Do not tighten the screws to allow for adjustment of the rail
!

## Slide 23: Rail module mounting
Important: If the transition between straight and curve does not fit well it may push out the pin between straight and curve rail.
Important: If the pins between curve rail and curve motor module will not fit you may leave them out
Shorter pins Pin D5x8 A2 DIN 7
(lower HW28)
Do not tighten the screws to allow for adjustment of the rail
!

## Slide 24: Rail module mounting
Construction after mounting the straight rails
  Pin D4x16 A2 DIN 7

## Slide 25: Rail module mounting
Now tighten the screws to the specified torque in this sequence:
1st - two curved rails with 2x 4 Screw M4x40 4Nm
2nd - two curved motor modules with 2x 3 Screw M5x30 6Nm
3rd - the straight rails with 22x Screw M4x40 4Nm
4th - the straight modules with 24x Screw M5x20 6Nm

## Slide 26: Agenda | XTS- Assembly
XTS-StarterKit
Preparation and Assembly
First Test
Rail mounting
Rerailing of Mover

## Slide 27: Mover and Rail
Construction after mounting the curved rails
Close the red auxiliary lock cover
  Pin D4x12 A2 DIN 7
  Screw M4x10 Cyl. A2 DIN 91
Important: Don’t forget the pins for the gate

## Slide 28: Mover and Rail
Construction after mounting the curved rails
Connect curved and straight rail
  Screw M3x30 A2 DIN 912
  Washer M3x30 A2 DIN 125
  Nut M3 A2 DIN 985
Important: Don't forget the screws for connecting

## Slide 29: Mover and Rail
It may be necessary to remove on motor module screw for easy insertion of the mover (lower HW22)
Insert the Mover
Attention: The encoder flag should be on the same side as the XTS sensor (not the side of the name plate and LEDs)

## Slide 30: Mover and Rail
Remove the red auxiliary lock cover to replace the lock cover again,
  Pin D4x12 A2 DIN 7
  Screw M4x10 Cyl. A2 DIN 91
Important: Don’t forget the pins for the gate
Notes: Note for photo text:
“Encoder flag must be on the same side as the XTS sensor (opposite the printed nameplate and LEDs).”

## Slide 31: XTS | New Freedom in Machine Building
Complex sequences – simplified solution: XTS

## Slide 32: Training material
This training material is provided to complement the presented training content. Outside the actual training the material may only be used for internal purposes at the company of the course participant. In addition, the material or extracts thereof may be used in end customer training for products containing Beckhoff products, or for presentations, provided the presentation refers to Beckhoff products. Extracts or copies of the training material must contain the following copyright acknowledgement: “© Beckhoff Automation GmbH & Co. KG”.
The same applies to extracts from presentation material. The user of the material is solely responsible for the completeness of extracts and copies. It is explicitly not permitted to offer commercial or free training for Beckhoff products. This applies to training with and or without the training material. The training material must not be edited, manipulated or modified.
Passing on of the aforementioned rights to third parties is not permitted.
Beckhoff Automation GmbH & Co. KG

## Slide 33
02/2021