## Slide 1: New Automation Technology Beckhoff Automation

## Slide 2: XTS Training

## Slide 3: XTS – TcIoXtsProcessingUnit (XPU)

## Slide 4: Agenda | XTS- TcIoXtsProcessingUnit (XPU)
XPU Introduction
XTS Configuration Process
XPU – Deep Dive
XTS Viewer
Mover 1
Simulation Mode

## Slide 5: XPU Introduction
TcIoXtsProcessingUnit as TcCOM Module (TwinCAT Component Object Models
TF5850 | TC3 XTS Extension
  Included TcIoXtsProcessingUnit
    TcIoXtsDrv (obsolete)
    SoftDrive
  TF5400 | TC3 Advanced Motion Pack
    Included
      TC3 Collision Avoidance

## Slide 6: XPU Introduction
TcIoXtsProcessingUnit is the link between the Motion and the hardware.
Axis
SoftDrive
Mover
Is controlled as a typical PTP axis by the PLC.
Represents the IO of the axis.
Contains the velocity and position control loops.
Represents a mover.
Calculate an absolute position and write a current.
Hardware
Contains the current control loop.
Has many position sensors.
SoftDrive
Motion
XPU
Devices
Module
Represents a motor-module.
Send the current setpoint toe the coils.
{

## Slide 7: XPU Introduction
Collects the input channels of all terminals and calculates an absolute position for each mover. (It knows the XTS topology.)
Forwards the current output of the controller (SoftDrive) to the individual coils which are activated by a mover.
Handles module boundaries smoothly.
The abstract components of one XTS module

## Slide 8: Agenda | XTS- TcIoXtsProcessingUnit (XPU)
XPU Introduction
XTS Configuration Process
XPU – Deep Dive
XTS Viewer
Mover 1
Simulation Mode

## Slide 9: XTS Configuration Process...
Start with a new project.
Perform a ‘Scan’ of the IO…
TIP
  After scan, change to Free-Run mode and have a look at the signals, the values should be changing continuously.

## Slide 10: XTS Configuration Process...
Open XTS Tool Window

## Slide 11: XTS Configuration Process...
Start the configuration process

## Slide 12: XTS Configuration Process...
Add XTS Task 1

## Slide 13: XTS Configuration Process...
Add XTS Parts

## Slide 14: XTS Configuration Process...
Add XTS Tracks (one track minmum)
Add Parts to the track

## Slide 15: XTS Configuration Process...
Add XTS Station (only display at the moment)
Info
  At the moment not necessary

## Slide 16: XTS Configuration Process...
Add XTS Mover

## Slide 17: XTS Configuration Process...
Add XTS Mover
  Mover List and Mover Details

## Slide 18: XTS Configuration Process...
Add XTS Mover
  choose names for Mover, Axis and Softdrive

## Slide 19: XTS Configuration Process...
Finished Configuration process

## Slide 20: XTS Configuration Process...
Finished Configuration process
The manager creates the configuration of the system:
Creates the XTS task.
Creates the child objects of the TcIoXtsProcessingUnit (modules & movers)
Adds the Movers to the NC configuration (with a SoftDrive object for each mover)
Context (task) of all XPU objects and SoftDrive objects are set.

## Slide 21: XTS Configuration Process...
Complete the configuration
Info
  Module objects are linked with the IO.
  Mover objects are linked with the SoftDrive.

## Slide 22: XTS Configuration Process...
Communication between the Modules:
  via Data Pointers
  No mapping object
  No copy process
Warning
  Use of data pointers is very fast but if used incorrectly data may be corrupted…

## Slide 23: XTS Configuration Process...
Manual settings Real-Time
  Change base time to 250 µs.
  Change XTS task settings.

## Slide 24: XTS Configuration Process...
Suggested settings Real-Time (small XTS-Systems)
  It is suggested to use one core just for the fast 250 µs XTS task (100% isolated).
  use 1 core just for windows and three cores as isolated real time cores

## Slide 25: XTS Configuration Process...
Manual settings XTS Task
  Change Cycle time to 250 µs
  Port must be greater or equal to 350
  ‘Create symbols’ is useful to simplify measurements with TC3 Scope

## Slide 26: XTS Configuration Process...
First activation…

## Slide 27: XTS Configuration Process...
First activation…
  Output Window

## Slide 28: XTS Configuration Process...
Teaching Process
Analog position signal of an XTS-Module
Before
After

## Slide 29: XTS Configuration Process...
Teaching Process
Before
After
Info
  In the case of newer XTS-System (HW 18), the analogue offset sets are stored in the XTS modules.
  A teaching process is not necessary

## Slide 30: XTS Configuration Process...
Teaching Process | first Step
  set a number for the teaching file which represents the current date.
Info
  Changes to the ‘TeachingFileNumber’ are not recognized until after an ‘Activate Configuration’ is performed.
  Before the teaching procedure is started, it must be activated so that the teaching data is saved in the correct file

## Slide 31: XTS Configuration Process...
Teaching Process | next Step
Move the Mover to a defined Position
Define Exclude Specified Items.
Info
  .selectionString Format X, Y, Z or X-Z
Position
Module 1
Module 2

## Slide 32: XTS Configuration Process...
Teaching Process | next Step
StartStandStillTeaching
Position
Module 1
Module 2

## Slide 33: XTS Configuration Process...
Teaching Process
Teaching Stops automatically
Position
Module 1
Module 2

## Slide 34: XTS Configuration Process...
Teaching Process | next Step
Move the Mover to a different defined Position
Change “.teachingSelection”
Warning
  Do not place movers at crossings where the module is active during teaching. Otherwise the feedback system will not work correctly.
Position
Module 1
Module 2

## Slide 35: XTS Configuration Process...
Teaching Process | next Step
StartStandStillTeaching
Position
Module 1
Module 2

## Slide 36: XTS Configuration Process...
Teaching Process
Teaching Stops automatically
Position
Module 1
Module 2

## Slide 37: XTS Configuration Process...
Teaching Process
  Set TwinCAT in Config Mode
Advice: Make a backup after the teaching file is created the first time

## Slide 38: XTS Configuration Process...
Teaching Process
  Set TwinCAT in Run-Mode

## Slide 39: Agenda | XTS- TcIoXtsProcessingUnit (XPU)
XPU Introduction
XTS Configuration Process
XPU – Deep Dive
XTS Viewer
Mover 1
Simulation Mode

## Slide 40: XPU - Deep Dive
TcIoXtsProcessingUnit is the link between the Motion and the hardware.
Axis
SoftDrive
Mover
Is controlled as a typical PTP axis by the PLC.
Represents the IO of the axis.
Contains the velocity and position control loops.
Represents a mover.
Calculate an absolute position and write a current.
Hardware
Contains the current control loop.
Has many position sensors.
SoftDrive
Motion
XPU
Devices
Module
Represents a motor-module.
Send the current setpoint toe the coils.
{

## Slide 41: XPU - Deep Dive
Cycle Update of SoftDrive & Axis
EtherCAT
AT2000-0250
AT2000-5250
AT2000-0250
AT2000-5250
SoftDrive 1
Axis 1
SoftDrive 2
Axis 2
SoftDrive 3
Axis 3
SoftDrive 4
Axis 4
Input / Output Update
NC-SAF Task (2ms)
XTS Task (250 µs)
Mover
Module
XPU

## Slide 42: XPU - Deep Dive
Real-Time Model
  click on Load Real-Time Model…

## Slide 43: XPU - Deep Dive
Real-Time Model
  Show the act. Real-Time Model
  Can use to adjust (better via Configurator)

## Slide 44: XPU - Deep Dive
Real-Time Model
  Create XTS Task 2 via Configurator

## Slide 45: XPU - Deep Dive
Real-Time Model
  Setup Real-Time

## Slide 46: XPU - Deep Dive
Real-Time Model
  Setup XTS Task 2

## Slide 47: XPU - Deep Dive
Real-Time Model
  new setup
Info
  This setup should not be used in a real machine. It is only an example.

## Slide 48: XPU - Deep Dive
Real-Time Model

## Slide 49: XPU - Deep Dive
Diagnosis
  output Window from Visual Studio

## Slide 50: XPU - Deep Dive
Diagnosis
  Module Diagnostic History

## Slide 51: XPU - Deep Dive
Diagnosis
  Parameter (Online)

## Slide 52: XPU - Deep Dive
Diagnosis
  Info's from EL9576 (Break Chopper Terminal)

## Slide 53: XPU - Deep Dive
Error Moverdetection
  Too few movers detected

## Slide 54: XPU - Deep Dive
Error Moverdetection
  Too many movers detected

## Slide 55: XPU - Deep Dive
Error Moverdetection
  Too few movers detected
  Too many movers detected

## Slide 56: XPU - Deep Dive
Collecting data…
  XTS-DUMP

## Slide 57: XPU - Deep Dive
Collecting data…
  XTS-SupportAssistant

## Slide 58: XPU - Deep Dive
Collecting data…
  XTS-SupportAssistant

## Slide 59: Agenda | XTS- TcIoXtsProcessingUnit (XPU)
XPU Introduction
XTS Configuration Process
XPU – Deep Dive
XTS Viewer
Mover 1
Simulation Mode

## Slide 60: XTS Viewer
XTS Viewer
  Start

## Slide 61: XTS Viewer
XTS Viewer
  Toolbar 1
open sup window
continuous update
connect to selected target
choose Target

## Slide 62: XTS Viewer
XTS Viewer
  Toolbar 2
choose a view description
Start / Stop view
select module side and rotation degree

## Slide 63: XTS Viewer
XTS Viewer
  Complete view

## Slide 64: XTS Viewer
XTS Viewer
  Show Mover Positions (Modulo Value)

## Slide 65: Agenda | XTS- TcIoXtsProcessingUnit (XPU)
XPU Introduction
XTS Configuration Process
XPU – Deep Dive
XTS Viewer
Mover 1
Simulation Mode

## Slide 66: Mover 1
Mover 1 functionality
The purpose of the Mover 1 detection is to identify a mover as a main mover and to distinguish it from the subsequent movers.
This offers then advantage of a clear correlation between mover hardware and software axis.

## Slide 67: Mover 1
Mover 1 functionality
Therefore one Mover with a special magnetic plate set is used (Mover1).
These magnets creates an inverted magnetic field.
This magnetic plate set exhibits a different behavior when the Mover1 search is triggered (MoverIdDetection)

## Slide 68: Mover 1
MoverldDetection
When MoverldDetection is trigger, all Movers make a small movement like "Wake and Shake".
Therefore 48V power supply is required.

## Slide 69: Mover 1
MoverldDetection
The mover detection across all movers is controlled via the TcloXtsProcessingUnit (XPU) object.
You have the option to apply general detection parameters
and to trigger the Mover 1 search manually.

## Slide 70: Mover 1
MoverldDetection
To use Mover ld detection the parameter "MoverldDetectionMode“ has to change to "Mover1 ".
When a Mover with the certain magnetic plate
is on the Track, this Parameter has to be
setup.
Otherwise this leads to unforeseen
movements of the mover.
Unforeseen movements can lead to injuries to
people and damage to tools and the
machine.

## Slide 71: Mover 1
MoverPositionAssignment
The absolute Position is setup regarding this
parameter.
lf the Parameter is set to "StartAtMover1"
the mover has the lowest or highest position,
dependent and the sorting order.

## Slide 72: Mover 1
MoverldDetectionMode
MoverPositionAssignment
Change of these parameters requires at TwinCAT
 Activate Configuration

## Slide 73: Mover 1
TriggerMoverIdDetection
By selecting the parameter
"TrigerMoverldDetection" and
,via right Mous-Click, download the
Parameter,
the Mover 1 detection is triggered manually

## Slide 74: Mover 1
Feedback Mover Id detection
Massages from the Mover ld detection
 shown in the Output Window
State of Mover ld detection
 as Parameter in "Parameter (Online)"

## Slide 75: Agenda | XTS- TcIoXtsProcessingUnit (XPU)
XPU Introduction
XTS Configuration Process
XPU – Deep Dive
XTS Viewer
Mover 1
Simulation Mode

## Slide 76: Simulation Mode
Simulation Mode
  Change Parameter „OperationMode“
  Setup Mover Simulation parameter
  Deactivate I/O Devices
  Activate Configuration

## Slide 77: Simulation Mode
Simulation Mode
  Setup Mover Simulation parameter

## Slide 78: Simulation Mode
Simulation Mode
  Simulation Mode Parameter

## Slide 79: XTS | New Freedom in Machine Building
Complex sequences – simplified solution: XTS

## Slide 80: Training material
This training material is provided to complement the presented training content. Outside the actual training the material may only be used for internal purposes at the company of the course participant. In addition, the material or extracts thereof may be used in end customer training for products containing Beckhoff products, or for presentations, provided the presentation refers to Beckhoff products. Extracts or copies of the training material must contain the following copyright acknowledgement: “© Beckhoff Automation GmbH & Co. KG”.
The same applies to extracts from presentation material. The user of the material is solely responsible for the completeness of extracts and copies. It is explicitly not permitted to offer commercial or free training for Beckhoff products. This applies to training with and or without the training material. The training material must not be edited, manipulated or modified.
Passing on of the aforementioned rights to third parties is not permitted.
Beckhoff Automation GmbH & Co. KG

## Slide 81
02/2021