## Slide 1: New Automation Technology Beckhoff Automation

## Slide 2: XTS Training

## Slide 3: XTS – TcSoftDrive

## Slide 4: Agenda | XTS- TcSoftDrive
Short XTS basics
XTS Accuracy
XTS IPC & capabilities
Scope for Mover monitoring
TcSoftdrive structure & parameter
Tuning

## Slide 5: XTS – Overview and timing
Analog Signal from Positions sensor
Coil current set-point
complete Control-Cycel
for all Mover
in 250µs
Position calculation
Velocity calculation
Position control
Velocity control
Transformation current set-point into coil set-current

## Slide 6: XTS – EtherCAT timing and data size
each Motor module has
15 Coils  15 current set-values  15 current act-values
2 Byte Status & 2 Byte Control
 32 Byte Process Image
each Sensor Module has
32 Position Sensors
2 Byte Status & 2 Byte Control
 66 Byte Process Image Input
EtherCAT data size 98 Byte

## Slide 7: XTS – EtherCAT timing and datasize
per Frame max. data size of 1500 Byte
per Module (Motor & Sensor)
data size of 98 Byte
3m XTS-Track  12 Modules
12 x 98 Byte = 1176 Byte Data
Full Frame size = 1264 Byte Data
Frame runtime = 103 µs

## Slide 8: XTS – Basic Timing
Notes: Erfassung der Wegmesssignale – Acquisition of the position feedback: 100KHz update rate
Mittelwert-bildung – Calculation
Verarbeitung in der Leistungselektronik – Processing in the power electronics: -32KHz Switching frequency – 300KHz current controller update rate

## Slide 9: XTS – TwinCAT integration
From the point of view of application programming, a mover looks like a „standard“ servo NC axis.
New standard tasks are available:
  Collision avoidance CA
  Group building
  Synchronous mechanisms
Runs on powerful Beckhoff Standard IPCs with EtherCAT-Port
Simulation mode is possible for TcSoftDrive

## Slide 10: XTS – TcSoftDrive control loop structure

## Slide 11: Agenda | XTS- TcSoftDrive
Short XTS basics
XTS Accuracy
XTS IPC & capabilities
Scope for Mover monitoring
TcSoftdrive structure & parameter
Tuning

## Slide 12: XTS - Definition of Accuracy
Ideal Positioning
Start Position
Target Position
High Accuracy
High Repeatability
Low Accuracy
High Repeatability
Low Accuracy
Low Repeatability
Low accuracy with high repeatability can be compensated.
Low repeatability cannot be compensated

## Slide 13: XTS - Position Accuracy (Sensor Rev. 18)
XTS Datasheet | 
Absolute Position Accuracy | ± 250µm (within one straight Module) *
Tested but not specified Accuracy | 
Achievable Position Accuracy | ± 150µm (within one straight Module) **
* Typical achievable absolute accuracy, this can become larger due to thermal expansion of the module (∆ϑ ≥ 30°C) or Parallelism of the flag to the encoder module and the orthogonality of the Encoder Flag to the Motor Module.
** typically achievable accuracy in a straight module between 15 - 235mm (Encoder flag completely in a single module) a parallel and orthogonal Encoder flag and a thermal expansion of while in operation (∆ϑ ≤ 15°C)
XTS Datasheet | 
Position accuracy while at speed | ± 150µm @ 1.5m/s (in a straight module) *
Tested but not specified Accuracy | 
Position accuracy while at speed in the curve | ± 400µm @ 1m/s (in a 180° Curve Module) **
* the synchronization accuracy is very dependent on the mechanical stiffness and the load on the mover and the controller settings. The mechanical displacement between the modules also plays an important role
** the deviation in the curve can be much, much worse if the center of gravity is not directly between the magnets of the mover
XTS Datasheet | 
Stand Still Repeatablity | ± 10µm (unidirectional) *
* repeatability for the encoder flag the stand still repeatability may fail due to the defects in the rail system or a Roller developing a flat spot or bearing failure or thermal extension

## Slide 14: XTS - Position Accuracy measurements
Chart: 
Absolute Position Accuracy measured against an very precise optical encoder

## Slide 15: XTS - Position Accuracy while moving
Measurement in the straight section at 1.5m/s with a tuned 12 Roller mover and no load
Position deviation in Lag Distance is less than ± 60µm

## Slide 16: XTS - Increasing Accuracy best Practices
Possible solutions if the accuraccy is not sufficient | 
Absolute accuracy of all Movers | Adapt the target position of the commands from the PLC based on previously measured and stored values. Mechanically position the tooling at the processing station, e.g. a pin to center the tooling. Use an External encoder feedback such as a laser distance sensor or a highly accurate quick Vision System - a balance during positioning would thereby therefore Possible
Absolute Accuracy between movers | Position offset in the NC. Each mover must be teached and a unique identification required External encoder or a laser distance sensor or a highly accurate quick Vision System - a correction during positioning would thereby also possible
Positional accuracy over several modules / synchronization accuracy | Setting a position offset in TcIoXts drivers per module (very time consuming) Sometimes AREA control parameters in TcSoftDrive can be adjusted to ensure a smoother ride Sometimes an additional counter-weight mass on the Mover can help bring the center of gravity to the middle of the magnets, thus improving the synchronous accuracy and travel through the curve

## Slide 17: Agenda | XTS-TcIoXts
Short XTS basics
XTS Accuracy
XTS IPC & capabilities
Scope for Mover monitoring
TcSoftdrive structure & parameter
Tuning

## Slide 18: XTS IPC & capabilities

## Slide 19: XTS – IPC C6930 Core™ i7 application examples

## Slide 20: XTS – IPC C6930 Core™ i7 current possible size

## Slide 21: XTS – Capabilities coming soon
Maximum circumference of 18 m
Maximum 80 movers on a track
Restrictions are purely due to data gathering and processing requirements
The mover count and circumference will continue to increase in coming years

## Slide 22: Agenda | XTS- TcSoftDrive
Short XTS basics
XTS Accuracy
XTS IPC & capabilities
Scope for Mover monitoring
TcSoftdrive structure & parameter
Tuning

## Slide 23: XTS TcSoftDrive – Scope for Mover monitoring

## Slide 24: XTS TcSoftDrive – Signal selection for monitoring

## Slide 25: XTS TcSoftDrive – Setup Motor-Parameter for monitoring
Change Parameter Motor.Type 1  2
- Variable Debug2 will be filled with InfeedPower
set “Show Hidden Parameter” first

## Slide 26: XTS TcSoftDrive – Trigger settings for monitoring

## Slide 27: XTS TcSoftDrive – Power monitoring example
Position [mm]
Velocity [mm/s]
Mover Current [A]
(this is different to the infeed current on the 48V DC!!!)
Acceleration [mm/s²]
Infeed Power [W]
FollowingError [mm]

## Slide 28: Agenda | XTS- TcSoftDrive
Short XTS basics
XTS Accuracy
XTS IPC & capabilities
Scope for Mover monitoring
TcSoftdrive structure & parameter
Tuning

## Slide 29: XTS TcSoftDrive

## Slide 30: XTS TcSoftDrive - parameter structure
General SoftDrive Parameter
  Parameter for Interpolator
  Parameter for Position calculation
  Parameter for Position Control
  Parameter for Velocity Control
  Parameter for Filter settings
  Parameter for feedforward control

## Slide 31: XTS TcSoftDrive - parameter structure

## Slide 32: XTS TcSoftDrive - parameter structure

## Slide 33: XTS TcSoftDrive - parameter structure

## Slide 34: XTS TcSoftDrive - parameter structure

## Slide 35: XTS TcSoftDrive - parameter structure

## Slide 36: XTS TcSoftDrive - parameter structure

## Slide 37: XTS TcSoftDrive - parameter structure

## Slide 38: XTS TcSoftDrive - parameter structure

## Slide 39: XTS TcSoftDrive - General SoftDrive Parameter

## Slide 40: XTS TcSoftDrive - 32 different control areas
1 up to 32 different control areas
Different parameter for position and velocity control
Different current limit could be set in Feedforward module
To use a certain control area [X].IsEnabled must be set to TRUE and Activate Configuration

## Slide 41: XTS TcSoftDrive - Interpolator

## Slide 42: XTS TcSoftDrive - Encoder

## Slide 43: XTS TcSoftDrive - position control

## Slide 44: XTS TcSoftDrive - parameter for position control
Type: P_Position
    only Kp is used
Type: P_Position_Standstill
Kp &
Kp_standstill is used
Type: P_Position_Standstill_Area
all parameter are used

## Slide 45: XTS TcSoftDrive - velocity control

## Slide 46: XTS TcSoftDrive - parameter for velocity control
Type: PI_Position
    only Kp & Tn is used
Type: PI_Velocity_Standstill Kp/Kp_standstill & Tn/Tn_standstill is used
Type: PI_Velocity_Standstill_Area
all Kp and Tn are used (standstill & area)

## Slide 47: XTS TcSoftDrive - parameter for velocity control
If one integral parameter is set to zero then the calculated value is also reset to zero.
If an old tmc is used the functionality is backward compatible

## Slide 48: XTS TcSoftDrive - filter parameter

## Slide 49: XTS TcSoftDrive - Feed Forward

## Slide 50: XTS TcSoftDrive - cyclic variables
From NC / PLC  TcSoftDrive
Mode: change TcSoftDrive operation mode & the use of the other cmd values
BipolarCurrentLimit: add the cyclic current limit value
AdditiveCurrentCmd: set an additional cyclic FFT current value. Functionality depends on the actual Operation mode used for real torque control
AdditiveCurrentCmd: add an additional cyclic FFT current value
ExtEncoderPosition: use position data from another source

## Slide 51: XTS TcSoftDrive - cyclic variables
From TcSoftDrive  NC / PLC
ActCurrentCmd: actual current command
ActHWPosModule: actual HW Position
ActFollowingError: actual Following Error

## Slide 52: XTS TcSoftDrive - setting for cyclic data
SoftDriveExternalEncoder
  These parameters set the encoder counting direction, the scaling and offset for the external encoder feedback. This external encoder position could also be the position from another XTS mover.
SoftDriveExternalDriveScale
  This parameter sets the scaling for the output of the actual SoftDrive current command e.g. for use with another drive HW

## Slide 53: Agenda | XTS- TcSoftDrive
Short XTS basics
XTS Accuracy
XTS IPC & capabilities
Scope for Mover monitoring
TcSoftdrive structure & parameter
Tuning

## Slide 54: XTS TcSoftDrive – Tuning
  Servo systems typically use a combination (cascaded) of three types of control loops:
  current loop (indirectly via the filter settings)
  velocity loop
  and position loop
  To tune the system, we have to tune each loop.
  Starting at the first loop (current indirectly via the filter settings )

## Slide 55: XTS TcSoftDrive – Tuning
Tuning Sequence
  Setup Filter Settings
    on the straight section
    on the curve section
  Setup Velocity-Control
    on the straight section
    on the curve section
  Setup Position-Control
    on the straight section
    on the curve section

## Slide 56: XTS TcSoftDrive – Tuning
Tuning Sequence
  Setup Filter Settings
    on the straight section
    on the curve section
  Setup Velocity-Control
    on the straight section
    on the curve section
  Setup Position-Control
    on the straight section
    on the curve section

## Slide 57: XTS TcSoftDrive – Tuning
Tuning Sequence
  Setup Filter Settings
    on the straight section
    on the curve section
  Setup Velocity-Control
    on the straight section
    on the curve section
  Setup Position-Control
    on the straight section
    on the curve section

## Slide 58: XTS TcSoftDrive – Tuning
Tuning Sequence
  Setup Filter Settings
    on the straight section
    on the curve section
  Setup Velocity-Control
    on the straight section
    on the curve section
  Setup Position-Control
    on the straight section
    on the curve section

## Slide 59: XTS TcSoftDrive – Tuning
Setup Filter Settings
To determine the Filter Settings there is a Tuning Assist
The Tuning Assist suggests values to adjust the filters and feedforward parameters
Typically only the Velocity and Position loops need to be tuned afterwards

## Slide 60: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
The Tuning Assist (TA) TcCom object is added to the existing TcSoftDrive module (Version ≥ 3.10.43.0)
The TA function operates in torque mode and generates a short current to the mover, followed by coasting to a stop. The Mover will be driven in both positive and negative directions and two measurements will be taken.
WARNING
Risk of injury from moving movers
When the Tuning Assist function is started the mover starts to move open loop with a jump. There is a risk of injury to body parts. Keep an appropriate safety distance, and stay clear outside of the operating space.

## Slide 61: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
The response of the system (Mover with tooling) will be measured and a Fast Fourier Transformation (FFT) is used to determine the frequency components
The result could be visualized with the array bar chart functionality of TwinCAT 3 Scope Views (Version ≥ 3.2.3136 starting with TwinCAT 3.1.4020.14)
WARNING
Risk of injury from moving movers
When the Tuning Assist function is started the mover starts to move open loop with a jump. There is a risk of injury to body parts. Keep an appropriate safety distance, and stay clear outside of the operating space.

## Slide 62: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
The behaviour (torsional oscillation) of the mechanical system is analyzed. The normal direction of motion for the application should be used to ensure the best parameterization of the control loops for optimal motion performance.
Notes: The scope view example shows the oscillation response over time when a current is applied to the mover.

## Slide 63: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
The direction of torsional oscillations is shown in the picture on the right by the red double arrow
The scope view example shows the oscillation response over time when a current is applied to the mover.
Notes: The scope view example shows the oscillation response over time when a current is applied to the mover.

## Slide 64: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
Add a TuningAssist object to an existing TcSoftDrive

## Slide 65: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
Set the context task of the TuningAssist object to the same XTS task the TcSoftDrive is using
Activate the configuration and restart TwinCAT
  In the Tuning Assist Obj. set the TcSoftDrive automatic parameter to Mode 10 (force mode)

## Slide 66: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
Create a new measurement project and choose “Scope Array Bar Project” as the type

## Slide 67: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
Add the array variable “SdTaBarChartVar2” to the Scope Axis

## Slide 68: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
Set the properties of the variable “SdTaBarChartVar2”:
  X Offset is set to 60 and
  X Scale Factor is set to 10
  The calculated frequency spectrum by the FFT is always calculated from 60 Hz to 600 Hz in 10 Hz steps

## Slide 69: XTS TcSoftDrive – Tuning Tuning Assist
Setup Position Leg Monitoring
Set the following error monitoring to a high value e.g. 500mm (or disable it)

## Slide 70: XTS TcSoftDrive – Tuning Tuning Assist
Determining Filter Settings using Tuning Assist
Process control is done by OnlineWrite and OnlineRead to the parameter “TuningProcess”
The Online-Value shows the actual state of the “TuningProcess”
TuningProcess Settings:
  TUNING_ASSIST_OFF
  START_MEASURE
  TUNING_ASSIST_ERROR
  BUSY_MEASURE
  DONE_MEASURE
  BUSY_SPEC_CALC1
  BUSY_SPEC_CALC2
  DONE_SPEC_CALC
  DONE_FILTER_CALC
  DONE_FRICTION_CALC
  ERROR_FRICTION_CALC

## Slide 71: XTS TcSoftDrive – Tuning Tuning Assist
The Tuning Assist object contain seven parameter
Parameter | Description
Tuning Type | Set the type of calculation – “Method1” measurement in move direction “Source2” measurement across move direction
Tuning Process | Status and control of the tuning assist procedure; set a new state with an “Online Write” access on this parameter and get the current state with an “Online Read” access on this parameter
Suggested_KpAccFFT | Suggestion for the acceleration feedforward gain “KpAccFFT” inside FeedForward_Obj6 after the complete tuning assist procedure was successful executed
Suggested_VeloFilterBandwidth | Suggestion for the “VelocityFilterBandwidth” inside the SoftDriveEncoder_Obj2 after the complete tuning assist procedure was successful executed
Suggested_LoadFilter | Suggestion for the load filter configuration inside the Filter_Obj5 after the complete tuning assist procedure was successful executed and this parameter was requested with an online read on this parameter
Suggested_Friction_Compensation | Suggestion for the parameter “FrictionCompensation” in Ampere, within the Feedforward object of the TcSoftDrive. To avoid following error, when changing the velocity, due to static friction
CurrentPulseTime | Set the time for the current pulse in ms. The default is 10ms but with higher load or more friction it is may necessary to increase it. The maximum possible time is 25 ms

## Slide 72: XTS TcSoftDrive – Tuning Tuning Assist
The Suggested parameter of the Tuning Assist
Parameter
Suggested_KpAccFFT
Suggested_LoadFilter
Suggested_VeloFilterBandwidth

## Slide 73: XTS TcSoftDrive – Tuning Tuning Assist
50% from Maximum
F1
F2
LPF
HPF
BW
This graphic shows how the calculation for the filter suggestion is done with one FFT result
LPF: LowPassFrequency
HPF: HighPassFrequency
BW: VelocityFilterBandwidth
Result of calculation

## Slide 74: XTS TcSoftDrive – Tuning Tuning Assist
50% vom
Maximum
F1
F2
Example 1:
If the two maxima are close to each other then one Bi-Quad Filter may be used
50% vom
Maximum
F1
Example 2:
If the maxima are too far apart, then a second order low pass filter is suggested

## Slide 75: XTS TcSoftDrive – Tuning Tuning Assist
Steps / Tips for Tuning Assist
  Enable the NC axis first and set the following error monitoring in the corresponding NC axis to a high value e.g. 500mm (or disable it)
  Execute some more measurements e.g. three on the straight and three on the curve and maybe also with / without product on the mover
  Analyze the spectrum manually as well and try to categorize the FFT with the given examples by yourself
  Notice the parameter suggestions and try to combine the filter settings
    Use lowest value for “Suggested_VeloFilterBandwidth
    Use lowest value for “Suggested_KpAccFFT” from a straight measurement
    Use LowpassFilter2 if both filter types are suggested (Lowpass2 & Biquad)
    Use lowest value for suggested “LowPassFreqeuncy”
    Use highest value for suggested “HighPassFreqeuncy”

## Slide 76: XTS TcSoftDrive – Tuning Velocity Control Loop
Velocity Control Loop
For velocity control loop a “PI” – Loop is used.
  Setup Kp
  Setup Tn

## Slide 77: XTS TcSoftDrive – Tuning Velocity Control Loop
Velocity Control Loop
Disable or remove the Tuning assist object (if not already done)
Set the SoftDrive “OperationMode” parameter in the main object to 9 (cyclic synchronous velocity mode)

## Slide 78: XTS TcSoftDrive – Tuning Velocity Control Loop
Velocity Control Loop
Set the following error monitoring to a high value e.g. 500mm (or disable it)

## Slide 79: XTS TcSoftDrive - velocity control
Velocity Control Loop
Switch off the integral part of the velocity control
  all Tn parameter set to zero

## Slide 80: XTS TcSoftDrive – Tuning Velocity Control Loop
Velocity Control Loop
Enable the NC axis and start the service mode “Velo Step Sequence”
Scope as minimum from the corresponding SoftDrive
  Act Velocity
  Set Velocity
  Set Current
May reduce the target velocity to avoid current saturation reaching the “MaxCurrentOutput” value (12A default)
WARNING
Risk of injury from moving movers
When the Velo Step Sequence function is started the mover starts to move open loop. There is a risk of injury to body parts. Keep an appropriate safety distance, and stay clear outside of the operating space.

## Slide 81: XTS TcSoftDrive – Tuning Velocity Control Loop (Kp)
Velocity Control Loop
Increase (or decrease) the velocity loop gain Kp until the actual velocity reaches 85 – 90 % of the commanded velocity (e.g. here 500 mm/s)
Set Kp_standstill parameter to the same value or a bit less e.g. 75%
Set Kp to reach 90% of command velocity

## Slide 82: XTS TcSoftDrive – Tuning Velocity Control Loop (Tn)
Velocity Control Loop
Switch on Tn with a large time value e.g. 0.2 s and reduce this incrementally until the actual velocity has a small overshoot of 5 – 10% of the command
Repeat procedure for the curve and use area parameters in case of differences in the straight and curve sections
Avoid saturating the current output
Set Tn to reach 5 -10 % overshoot

## Slide 83: XTS TcSoftDrive – Tuning Velocity Control Loop (Tn)
Velocity Control Loop
Repeat procedure for the curve and use area parameters in case of differences in the straight and curve sections
Avoid saturating the current output
Set Tn to reach 5 -10 % overshoot

## Slide 84: XTS TcSoftDrive – Tuning Position Control Loop
Position Control Loop
For position control loop a “P” – Controler is used.
  Setup Kp

## Slide 85: XTS TcSoftDrive – Tuning Position Control Loop
Position Control Loop
Set the SoftDrive “OperationMode” parameter in the main object to 8 (cyclic synchronous position mode)

## Slide 86: XTS TcSoftDrive – Tuning Position Control Loop
Position Control Loop
Set the following error monitoring back to “normal” values

## Slide 87: XTS TcSoftDrive – Tuning Position Control Loop
Position Control Loop
Enable the NC axis and start the service mode “Reversing Sequence” with achievable (or necessary) values for velocity, acceleration and jerk
Also scope the following error parameter of the SoftDrive

## Slide 88: XTS TcSoftDrive – Tuning Position Control Loop (Kp)
Position Control Loop
Increase Kp of position loop to reduce following error as much as possible but stop before getting more noise or oscillation
Set Kp_standstill parameter to the same value or maybe a bit less e.g. 75%
Repeat procedure for the curve and use area parameter in case of differences in the straight and curve

## Slide 89: XTS | New Freedom in Machine Building
Complex sequences – simplified solution: XTS

## Slide 90: Training material
This training material is provided to complement the presented training content. Outside the actual training the material may only be used for internal purposes at the company of the course participant. In addition, the material or extracts thereof may be used in end customer training for products containing Beckhoff products, or for presentations, provided the presentation refers to Beckhoff products. Extracts or copies of the training material must contain the following copyright acknowledgement: “© Beckhoff Automation GmbH & Co. KG”.
The same applies to extracts from presentation material. The user of the material is solely responsible for the completeness of extracts and copies. It is explicitly not permitted to offer commercial or free training for Beckhoff products. This applies to training with and or without the training material. The training material must not be edited, manipulated or modified.
Passing on of the aforementioned rights to third parties is not permitted.
Beckhoff Automation GmbH & Co. KG

## Slide 91
02/2021